## Slide 1
Kiyan Vadoudi
LCA and Circular Economy Specialist
Life Cycle Assessment of Carbios Enzymatic Bio-Recycling Technology: Powering PET Plastic and Textile Circularity​

## Slide 2
460 million tons (1)
of plastic produced
per year (2019)
> Plastic production
353 million tons (1)
of plastic waste generated
1. OECD iLibrary, 2022
> Extensive plastic pollution
8%
Recycling
Secondary plastics produced 29Mt
Plastic usage has created major environmental and health issues
3%
Closed-Loop
Notes: Plastic production and consumption have created significant environmental impacts, and one of the main reasons for this is the current end-of-life (EOL) management situation of plastic worldwide. As you can see, in 2019, only 8% was collected for recycling, and from that, only 3% underwent closed-loop recycling.
Post-consumer recycled plastics 11% in Europe – Plastics Europe
European virgin plastics production 87.6% (5.3% PET)
Closed-Loop recycling rate in Europe 3%

## Slide 3
Oil extraction and refining
Polymers production and conversion into plastic items
End of life of the majority of plastic waste today
1.8 gigatons of greenhouse gas (GHG) emissions (1)
Contribution of plastic industry in global warming
(GHG) emissions of Plastic production
(GHG) emissions of Plastic conventional End of Life
(2)
1. OECD iLibrary, 2022 2. Ecoinvent 3.8 (The EOL environmental impact of plastic varies depending on the proportions of landfill and incineration)
There’s no single solution:
We must implement the 4R principles “REDUCE, REUSE, RECYCLE and RECOVER”
Notes: The plastic industry contributes about 4% to global warming potential (GWP), with virgin material extraction and polymerization accounting for approximately 70% of this impact. There’s no single solution and we must implement “REDUCE, REUSE, RECYCLE”. To reduce the GWP of plastic, we need to take action for managing its lifecycle.
4% of Global emission

## Slide 4
Virgin PET
Production
Polyethylene terephthalate (PET) value chain and European market share
Contact Sensitive
(Food safety regulation2)
Non- Contact Sensitive
Pretreatment
37%
13%
7%
33%
Market Share (EU) 1
But Textile Global Market Share 60%-65%3
1. How circular is PET?, Zero Waste
2. European Commission
3. IHS Markit in 2021
9%
1%

## Slide 5
Recyclability of Food grade PET waste
By 2030, Europe wants all plastic packaging on the market to be 100% recyclable3
Today, only a small portion of PET waste is treated by mechanical recycling, with the rest (60%) ending up in incineration or landfill.
Mechanical process negatively impacts the chemical and mechanical properties.
1. Yin, S., et al.. Mechanical reprocessing of polyolefin waste: a review. , 2015
Virgin PET
Production
Pretreatment
3. European Commission
2. How circular is PET?, Zero Waste
Mechanical recycling
DOWN-RECYCLING

## Slide 6
https://renewable-carbon.eu/
Recycling technologies for PET waste
Open-loop
Methanolysis
Glycolysis
Notes: In general, there are three routes for PET recycling. One is open-loop recycling, which involves thermal treatment, and the other two routes can produce recyclate through physical treatment and depolymerization. Chemical treatment has been the major technology for monomer production, and recently, thanks to Carbios technology, a new route in this field has been introduced as biological treatment.

## Slide 7
Clermont-Ferrand
Headquarters
Process development
Demonstration Plant
Toulouse
Research center
PopLaB
Longlaville
PET biorecycling plant
Under construction
Preparing for operations
First products deliveries in 2026
3 sites
150 people
Carbios, a French biotech with international ambitions
Pr Alain Marty
(Chief Scientific Officer) and team
Enzyme development
Notes: Carbios is a French biotech pioneer in biorecycling of plastics with three sites: the headquarters, laboratory, pilot, and demonstration plants are located in Clermont-Ferrand in the center of France. Our research center is in Toulouse in collaboration with the University of Toulouse (TBI), and the plant under construction is in Loglaville, northeast of France, scheduled to commence operations in 2025.

## Slide 8
Two technologies to reinvent the life cycle of plastics and textiles
A world-first designed and developed by Carbios
Notes: The technology is simple: the developed enzymes are added to plastic and textile waste in a hydrolysis process. At the end of the process, we recover PTA and MEG, which are ready for virgin-quality polymerization. At Carbios, we also have another technology, Enzymed PLA (Polylactic acid), which increases the degradation of PLA. Our research center is working on other types of polymers such as Polypropylene (PP) and Polyamide (PA).

## Slide 9
Picoliter - Microliter
250 ml to 5 litres
20 M3
4 * 300 m3
1 M3
Enzyme identification and enzyme engineering
Process scaling
Pilot
Demonstration plant
1st commercial -scale project
1 batch / week
25 people, 3 shifts
5 days / week
20 M€ Capex
50 000 tons / year
~ 70 direct jobs
5 shifts, 7 / 7
230 M€ Capex
2011 – now
2014
2019
2021
2025
Carbios’ PET recycling technology: Steps towards commercialization
Projects under License
Notes: The Carbios project began in 2011 with the identification and engineering of enzymes. As part of the Life project for textiles, we entered the industrial demonstrator scale in 2021, managing 2 tons of waste. The future factory in Loglaville will manage 50,000 tons per year.

## Slide 10
Environmental impacts
&
Circularity assessment
Packaging & Textile
-90 % CO2 emissions vs one cycle of virgin PET production*
~95 ktons CO2/year savings
in the first plant at Longlaville*
* France scenario, taking into account diversion of 75% PET waste from a conventional end-of-life
Virgin PET: 2.9kg CO2/kg (cradle to gate), ecoinvent 3.10 base
Capacity of 50,000 tons of PET waste per year

## Slide 11
General methods
  Use of ISO 14040/14044 standard in cradle-to-gate LCA approach
  Goals
  Assessment of environmental impact of Carbios rPET produced from PET waste in Longlaville, France (currently under construction with 50000 ton/y capacity).
  Compare environmental impacts of Carbios’ rPET versus virgin PET produced in Europe
Since 2018, Carbios has been carrying out an environmental assessment of Carbios enzymatic technology for PET packaging using the LCA tool.
Goals and scope

## Slide 12
Wastes types
  Coloured and opaque bottles
  Mono and multilayer trays
  Residuals from mechanical recycling (fines)
Data Sources
  Process data from Material and Utilities balance of the Reference Unit ’s design
  Life cycle inventory (LCI) datasets: ecoinvent databases 3.10, ADEME 2022 and Franklin Association.
All PET waste that could not be treated by mechanical recycling to produce food-grade clear PET
Main assumptions and data sources
Functional Unit
  Production of 1 kg recycled PET of equivalent quality to virgin PET

## Slide 13
1. ISO 14040 et 14044
Overview of the system boundaries – Cradle-to-Gate
Pretreatment
Depolymerization
Filtration & discoloration
Separation of TA & MEG
MEG
PTA
3. CARBIOS specific steps
CARBIOS full process system boundary
Post consumer PET waste
4. PET production
1. Waste collection & sorting
2. Waste preparation
T
T
T
T
T
Transport
France
France (Longlaville)
The Netherlands (Rotterdam)
France
Functional unit = production of 1 kg of bottle-grade PET
Burden free

## Slide 14: -90 % CO2 emissions vs virgin PET production
Chart: Climate Change
| Catégorie 1
Virgin PET - Ecoinvent 3.10 Europe | 2.9
Carbios rPET | 2.2
Carbios rPET with 50% EOL substitution | 0.3
-24%
-90% CO2 emission vs Virgin PET
-90%
Europe
France
France

## Slide 15: Methodological approach #1 – Cut-off
Virgin PET
100% incineration
1,6 kg CO2-eq/kg PET waste
2,9 kg CO2-eq/kg PET
2,2 kg CO2-eq/kg PET
-24%
rPET
Carbios
rPET
Flakes preparation
Virgin PET
2,9 kg CO2-eq/kg PET
Cut-off: only the recycling process
Only the material production is considered

## Slide 16: Methodological approach #2 – Substitution
Flakes preparation
rPET
100% incineration
- 2,55 kg CO2-eq/1,53 kg PET waste
Virgin PET
2,9 kg CO2-eq/kg PET
-90%
2,9 kg CO2-eq/kg PET
Carbios
rPET
Virgin PET
75%
0,3 kg CO2-eq/kg PET
Substitution: PET value chain
This approach takes into consideration the two main functions of the recycling process: material recovery & diverting waste from conventional End-of-Life

## Slide 17: Global warming potential of Carbios recycling technology
Comparisons of Carbios rPET vs Virgin PET
Chart: kg CO2-eq/kg PET
| Catégorie 1
Colonne1
Série 1 | 2.2
Série 2 | 0.3
Série 3 | 2.9
Substitution Co-Products
Collection and Sorting
Flakes production
Carbios specific Process (MEG and PTA production)
Polymerization
Chart: 
| Catégorie 1
Série 1 | 0.13
Série 2 | 0.45
Série 3 | 1.67
Serie 4 | 0.32
-24%
-90%
European Virgin PET
Ecoinvent 3.10
Carbios rPET
Cut-off
Carbios rPET with
75% EOL substitution
Notes: Add Carbios and substitution

## Slide 18
1. Heat source
Current: Natural gas produce 0,5 kg CO2-eq/kg rPET
Target: On site (biomass + CSR) boiler
Potential for decrease CO2 emission : -29%
2. Enzyme
Improvement in the efficiency of enzyme production
3- Process Improvement
Short term opportunities for CO2 emission reduction

## Slide 19
Carbios is bringing to the market an enzymatic hydrolysis technology with high circularity performance
  High recyclability and Robust on design and performances with complex feedstock
  Recovery yield > 85%
  Produced monomers can be used in their initial or any applications
The full potential on CO2 emissions is captured by combining
  Not only chemical recycling process but the overall value chain
  Chemical recycling is seen today as the only alternative to conventional end of Life for complex feedstocks
  CO2 impact of the value chain with Carbios block inside is 90% less than fossil-based linear system, with the integration of 75% End of Life substitution
Perspectives:
The future will be a combination of Virgin, Mechanical recycling and Chemical recycling
 combination of LCA and circularity, due to the limits of current LCA
Conclusions and perspective

## Slide 20: Thank you for your attention
Kiyan VADOUDI : kiyan.vadoudi@carbios.com